## Slide 1
CTS Cohort 6 | RCS07 | Day 15 | July 29, 2026
RCS Day 7
Integrated wall QC, punch-list correction, retest, evidence, and handoff
CORRECT. COMPLETE. PROVE.
A complete wall is safe, accurate, inspectable, and explainable.
Today the goal is not to hide defects. The goal is an honest punch list and verified corrections.
1
Notes: Open with the corrected lab mission. All kits remain disconnected until approval.

## Slide 2
CTS Cohort 6 | RCS07 | Day 15 | July 29, 2026
Today's flow
Quiz -> model -> guided practice -> capstone lab -> QC
Quiz
10:15
QC model
10:50
Punch list
11:20
Handoff
12:00
Rework
1:00
Retest
2:25
Exit
2:45
Morning: inspect subsystems, write punch items, and plan evidence.
Afternoon: complete approved rework and close one documented defect.
End: whole-wall QC, handoff practice, evidence, reset.
2
Notes: Use this to keep Rich and students oriented.

## Slide 3
CTS Cohort 6 | RCS07 | Day 15 | July 29, 2026
Today's targets
What successful work must demonstrate
Framing
geometry
Window
opening
Two outlets +
switch/light
Drywall
fit + fasteners
Labels +
evidence
Complete remaining capstone framing, electrical, and drywall work
Run a subsystem and whole-wall QC inspection
Diagnose and correct one documented defect
Prepare a professional handoff package
3
Notes: Emphasize the inverter is not a tiny controller load.

## Slide 4
CTS Cohort 6 | RCS07 | Day 15 | July 29, 2026
The day's path
Trace the work before building it
Baseline
inspection
Punch list
Approved
rework
Retest +
evidence
Handoff
Prioritize safety and functional defects first. Unresolved items remain visible in the handoff.
4
Notes: Ask students to point out positive and negative paths.

## Slide 5
CTS Cohort 6 | RCS07 | Day 15 | July 29, 2026
Controlled sequence
Release each stage only after its check
1
Inspect subsystems
2
Prioritize punch list
3
Correct one defect
4
Retest + handoff
Reapply the right tool and energy controls before every correction. Rework does not suspend safety boundaries.
5
Notes: Say “most controllers” because manuals vary. Teach general practice plus verify equipment.

## Slide 6
CTS Cohort 6 | RCS07 | Day 15 | July 29, 2026
Working roles
6 students; every result receives another set of eyes
Owner
performs approved rework
Inspector
checks acceptance criteria
Documenter
captures before/after proof
Each student owns their capstone result.
Peer inspection adds another set of eyes; instructor approval closes the item.
State unresolved work honestly.
6
Notes: This matches the actual five-kit/six-student constraint.

## Slide 7
CTS Cohort 6 | RCS07 | Day 15 | July 29, 2026
Verification checkpoints
Do not trust appearance alone
Framing + window
Electrical mock-up
Drywall + fasteners
Labels + evidence
Inspect each subsystem, then the integrated wall.
A punch item closes only after correction and a defined reinspection or retest.
7
Notes: Have students practice the measurement sentence.

## Slide 8
CTS Cohort 6 | RCS07 | Day 15 | July 29, 2026
Safety boundaries
The lab begins only inside these controls
Task controls reset
No energized work
Rework zone isolated
Stop outside scope
Instructor approval is required before reopening covered or terminated systems. Stop if a correction creates a new hazard or exceeds training scope.
8
Notes: Do not overdo calculations today. Keep the principle concrete.

## Slide 9
CTS Cohort 6 | RCS07 | Day 15 | July 29, 2026
Professional judgment
Safe work pauses when the evidence conflicts
Good handoff
show condition -> evidence -> result
Bad handoff
hide defects -> claim complete
Professional documentation includes unresolved items. Trust comes from traceability, not presentation polish alone.
9
Notes: Unless the equipment manual says otherwise, teach inverter battery-side with protection.

## Slide 10
CTS Cohort 6 | RCS07 | Day 15 | July 29, 2026
Quality criteria
Good physical work leaves visible proof
Inspect framing, devices, drywall, and labels.
Write specific punch items by location.
Correct approved work under task controls.
Retest against acceptance criteria.
Capture overall, detail, test, and corrected views.
No retest evidence? The punch item stays open.
10
Notes: Make rework normal. Bad crimps are data. Hidden bad crimps are future pain.

## Slide 11
CTS Cohort 6 | RCS07 | Day 15 | July 29, 2026
Lab release checklist
The station earns work only after the checks
Pre-task plan and energy state complete.
Baseline whole-wall inspection recorded.
Punch list identifies locations and owners.
Safety/functional items prioritized first.
Rework scope approved by instructor.
Evidence device and file names ready.
11
Notes: Use this slide as the afternoon pass standard.

## Slide 12
CTS Cohort 6 | RCS07 | Day 15 | July 29, 2026
Afternoon lab
Slow sequence. Clear callouts. No surprises.
1
Inspect + punch
2
Prioritize + approve
3
Rework + subsystem QC
4
Retest + whole-wall QC
Complete the individual capstone, close at least one documented punch item, and prepare a 60-second handoff.
12
Notes: Keep control of the final power-up moment.

## Slide 13
CTS Cohort 6 | RCS07 | Day 15 | July 29, 2026
Closeout order
End verified, documented, and reset
1
Overall photo
2
Defect detail
3
Correction + retest
4
Handoff + reset
Handoff includes scope, key decisions, verified results, evidence, and any unresolved items.
13
Notes: Use this before cleanup so the room ends clean.

## Slide 14
CTS Cohort 6 | RCS07 | Day 15 | July 29, 2026
Evidence log
What students write down
Frame
dims + square
Pass: ________
Devices
2 outlets + S/L
Pass: ________
Drywall
fit + fasteners
Pass: ________
Punch item
location + defect
ID: __________
Retest
acceptance check
Result: _______
Handoff
evidence indexed
Ready: ________
A polished surface does not close a defect. Evidence and a defined retest do.
14
Notes: Match the worksheet measurement log.

## Slide 15
CTS Cohort 6 | RCS07 | Day 15 | July 29, 2026
Exit ticket
Three checks before dismissal
1. Name your highest-priority punch item.
2. Describe the correction and its retest evidence.
3. State any unresolved item honestly.
Punch list current. Corrections verified. Evidence indexed. Wall ready.
15
Notes: Collect tickets and use them to decide what Day 5 needs.