## Slide 1
CTS Cohort 6 | RCS04 | Day 12 | July 23, 2026
RCS Day 4
Supply, DWV, P-trap assembly, dry verification, and system coordination
ALIGN FIRST. TIGHTEN SECOND.
Dry classroom verification only unless the instructor controls a separate test.
Today the goal is not to force fittings together. The goal is an aligned, explainable path.
1
Notes: Open with the corrected lab mission. All kits remain disconnected until approval.

## Slide 2
CTS Cohort 6 | RCS04 | Day 12 | July 23, 2026
Today's flow
Quiz -> model -> guided practice -> capstone lab -> QC
Quiz
10:15
System map
10:50
Trap demo
11:20
Dry checks
12:00
Build
1:00
Fault-find
2:25
Exit
2:45
Morning: separate supply from drain-waste-vent functions.
Afternoon: dry-fit, inspect, fault-find, correct, and map a capstone path.
End: parts identified, fault documented, station dry and reset.
2
Notes: Use this to keep Rich and students oriented.

## Slide 3
CTS Cohort 6 | RCS04 | Day 12 | July 23, 2026
Today's targets
What successful work must demonstrate
Supply
pressure
Shutoff
isolation
Fixture
use point
P-trap
seal
DWV
gravity path
Differentiate supply and drain-waste-vent functions
Explain fixture, trap, and shutoff roles
Plan a training plumbing path through framing
Assemble and troubleshoot a dry rolling-sink/P-trap module
3
Notes: Emphasize the inverter is not a tiny controller load.

## Slide 4
CTS Cohort 6 | RCS04 | Day 12 | July 23, 2026
The day's path
Trace the work before building it
Supply
Shutoff
Fixture
Tailpiece +
P-trap
Trap arm +
drain
Trace pressure toward the fixture and gravity away from it. Keep the full path accessible for inspection.
4
Notes: Ask students to point out positive and negative paths.

## Slide 5
CTS Cohort 6 | RCS04 | Day 12 | July 23, 2026
Controlled sequence
Release each stage only after its check
1
Inventory parts
2
Dry-fit path
3
Align + hand assemble
4
Inspect + troubleshoot
Orient washers before tightening. Correct cross-threading or damaged parts instead of applying more force.
5
Notes: Say “most controllers” because manuals vary. Teach general practice plus verify equipment.

## Slide 6
CTS Cohort 6 | RCS04 | Day 12 | July 23, 2026
Working roles
6 students; every result receives another set of eyes
Builder
assembles path
Inspector
checks parts + alignment
Documenter
maps + records fault
Rotate after the first dry assembly.
The Inspector names each part and checks thread start, washer orientation, and access.
Change one condition at a time.
6
Notes: This matches the actual five-kit/six-student constraint.

## Slide 7
CTS Cohort 6 | RCS04 | Day 12 | July 23, 2026
Verification checkpoints
Do not trust appearance alone
Correct parts
Washer orientation
Threads start clean
Path aligned + accessible
Inspect before tightening.
A reliable diagnosis records expected condition, observed condition, one correction, and a dry recheck.
7
Notes: Have students practice the measurement sentence.

## Slide 8
CTS Cohort 6 | RCS04 | Day 12 | July 23, 2026
Safety boundaries
The lab begins only inside these controls
No uncontrolled water
Electrical zone separate
No unapproved drilling
Stop damaged parts
Wipe unexpected moisture immediately. Keep cords and electrical equipment out of the plumbing station. No structural penetration without approval.
8
Notes: Do not overdo calculations today. Keep the principle concrete.

## Slide 9
CTS Cohort 6 | RCS04 | Day 12 | July 23, 2026
Professional judgment
Safe work pauses when the evidence conflicts
Good path
dry-fit -> align -> tighten -> inspect
Bad habit
force threads -> hide leak path
Cross-threading and misaligned washers do not improve with confidence. Stop, disassemble, identify the fault, and correct it.
9
Notes: Unless the equipment manual says otherwise, teach inverter battery-side with protection.

## Slide 10
CTS Cohort 6 | RCS04 | Day 12 | July 23, 2026
Quality criteria
Good physical work leaves visible proof
Inventory every fitting and washer.
Trace supply and drain paths separately.
Start slip nuts by hand.
Keep joints aligned and accessible.
Correct one fault, dry-reverify, and document.
Part does not seat? Stop forcing it.
10
Notes: Make rework normal. Bad crimps are data. Hidden bad crimps are future pain.

## Slide 11
CTS Cohort 6 | RCS04 | Day 12 | July 23, 2026
Lab release checklist
The station earns work only after the checks
Module inventory complete.
Supply and drain paths traced.
Parts inspected for cracks or damage.
Washers oriented before assembly.
No water/pressure test without authorization.
Capstone path avoids electrical boxes.
11
Notes: Use this slide as the afternoon pass standard.

## Slide 12
CTS Cohort 6 | RCS04 | Day 12 | July 23, 2026
Afternoon lab
Slow sequence. Clear callouts. No surprises.
1
Map + inventory
2
Dry-fit + assemble
3
Diagnose one fault
4
Correct + dry-recheck
Rebuild the rolling sink/P-trap module, then map a coordinated plumbing pathway on the capstone wall.
12
Notes: Keep control of the final power-up moment.

## Slide 13
CTS Cohort 6 | RCS04 | Day 12 | July 23, 2026
Closeout order
End verified, documented, and reset
1
Name the fault
2
Record evidence
3
Correct one issue
4
Dry-reverify + reset
Keep the station dry. Record the part, condition, correction, and result before returning the module.
13
Notes: Use this before cleanup so the room ends clean.

## Slide 14
CTS Cohort 6 | RCS04 | Day 12 | July 23, 2026
Evidence log
What students write down
System map
supply + drain
Done: ________
Parts
correct + sound
Pass: ________
Washers
orientation
Pass: ________
Threads
clean start
Pass: ________
Alignment
accessible path
Pass: ________
Capstone
coordinated route
Sketch: _______
No dry inspection, no approval. Alignment is easiest to correct before tightening.
14
Notes: Match the worksheet measurement log.

## Slide 15
CTS Cohort 6 | RCS04 | Day 12 | July 23, 2026
Exit ticket
Three checks before dismissal
1. Draw the fixture-to-drain path through the P-trap.
2. Name one fault and the evidence that revealed it.
3. State today's water and drilling boundaries.
Module dry. Parts counted. Fault documented. Station reset.
15
Notes: Collect tickets and use them to decide what Day 5 needs.