## Slide 1
CTS Cohort 6 | RCS02 | Day 10 | July 21, 2026
RCS Day 2
Framing layout, wall members, supervised cutting, and square checks
MEASURE. MARK. VERIFY. CUT.
6 capstone walls. One approved drawing. Every cut gets a second check.
Today the goal is not to build fast. The goal is a square, traceable frame.
1
Notes: Open with the corrected lab mission. All kits remain disconnected until approval.

## Slide 2
CTS Cohort 6 | RCS02 | Day 10 | July 21, 2026
Today's flow
Quiz -> model -> guided practice -> capstone lab -> QC
Quiz
10:15
Tape skills
10:50
Wall map
11:20
Cut list
12:00
Build
1:00
QC
2:25
Exit
2:45
Morning: read to 1/16 inch and map every wall member.
Afternoon: build one individual window-wall frame under tool control.
End: dimensions, diagonals, fasteners, labels, photo, reset.
2
Notes: Use this to keep Rich and students oriented.

## Slide 3
CTS Cohort 6 | RCS02 | Day 10 | July 21, 2026
Today's targets
What successful work must demonstrate
Tape
1/16 inch
Plates +
studs
King + jack
studs
Header +
sill
Square +
evidence
Read a tape measure to 1/16 inch and add common fractions
Identify plates, studs, king studs, jack studs, header, sill, and cripples
Lay out a 4-foot by 3-foot training wall with a framed window opening
Complete an instructor-approved cut list and assemble a square wall frame
3
Notes: Emphasize the inverter is not a tiny controller load.

## Slide 4
CTS Cohort 6 | RCS02 | Day 10 | July 21, 2026
The day's path
Trace the work before building it
Approved
drawing
Measure
stock
Mark +
verify
Cut +
dry-fit
Fasten +
check square
A second set of eyes checks the mark before the saw starts. Conflicting measurements stop the work.
4
Notes: Ask students to point out positive and negative paths.

## Slide 5
CTS Cohort 6 | RCS02 | Day 10 | July 21, 2026
Controlled sequence
Release each stage only after its check
1
Inventory + drawing
2
Approved cut list
3
Dry-fit + assemble
4
Dimensions + diagonals
Keep the frame flat through assembly. Correct layout or square before moving to the next system.
5
Notes: Say “most controllers” because manuals vary. Teach general practice plus verify equipment.

## Slide 6
CTS Cohort 6 | RCS02 | Day 10 | July 21, 2026
Working roles
6 students; every result receives another set of eyes
Builder
measures + assembles
Inspector
checks marks + square
Documenter
records + photographs
Rotate roles at the instructor checkpoint.
The Builder does not approve their own critical mark.
Say measurements out loud and record the final result.
6
Notes: This matches the actual five-kit/six-student constraint.

## Slide 7
CTS Cohort 6 | RCS02 | Day 10 | July 21, 2026
Verification checkpoints
Do not trust appearance alone
Tape reading
Member labels
Diagonal A / B
Fasteners + edges
Call the measurement, reference edge, and mark before cutting.
Match diagonals and verify overall dimensions.
Inspect fastener placement and lumber condition before approval.
7
Notes: Have students practice the measurement sentence.

## Slide 8
CTS Cohort 6 | RCS02 | Day 10 | July 21, 2026
Safety boundaries
The lab begins only inside these controls
Eyes + hearing
Guards remain on
Clamp / support stock
Cut approval
Inspect lumber and tools before use. Keep body position out of the cut path. Stop for damaged stock, conflicting marks, or a missing guard.
8
Notes: Do not overdo calculations today. Keep the principle concrete.

## Slide 9
CTS Cohort 6 | RCS02 | Day 10 | July 21, 2026
Professional judgment
Safe work pauses when the evidence conflicts
Good path
measure -> mark -> verify -> cut
Stop-work path
conflict -> pause -> resolve
Speed never outranks control. A wrong cut wastes material; an unsafe cut can injure a person. Ask before guessing.
9
Notes: Unless the equipment manual says otherwise, teach inverter battery-side with protection.

## Slide 10
CTS Cohort 6 | RCS02 | Day 10 | July 21, 2026
Quality criteria
Good physical work leaves visible proof
Read the plan before touching stock.
Use one reference edge and a clear carpenter's mark.
Dry-fit members in position.
Check overall dimensions and both diagonals.
Label, photograph, and reset the station.
Unverified mark? Do not cut it.
10
Notes: Make rework normal. Bad crimps are data. Hidden bad crimps are future pain.

## Slide 11
CTS Cohort 6 | RCS02 | Day 10 | July 21, 2026
Lab release checklist
The station earns work only after the checks
PPE and station inspected.
Training drawing identified.
Cut list complete and labeled.
Critical marks partner-verified.
Instructor authorizes each cut.
Frame remains supported and controlled.
11
Notes: Use this slide as the afternoon pass standard.

## Slide 12
CTS Cohort 6 | RCS02 | Day 10 | July 21, 2026
Afternoon lab
Slow sequence. Clear callouts. No surprises.
1
Plan + cut list
2
Mark + verify
3
Cut + assemble
4
Square + document
Build the individual 4 ft x 3 ft capstone wall with framed window opening. Supervised cuts only after clearance.
12
Notes: Keep control of the final power-up moment.

## Slide 13
CTS Cohort 6 | RCS02 | Day 10 | July 21, 2026
Closeout order
End verified, documented, and reset
1
Check dimensions
2
Compare diagonals
3
Correct + recheck
4
Photo + reset
A finished-looking frame is not enough. Record the numbers that prove the wall meets the approved training drawing.
13
Notes: Use this before cleanup so the room ends clean.

## Slide 14
CTS Cohort 6 | RCS02 | Day 10 | July 21, 2026
Evidence log
What students write down
Drawing
approved version
Initials: ______
Cut list
qty + length
Approved: _____
Diagonal A
corner to corner
Value: _______
Diagonal B
corner to corner
Value: _______
Window
dims + square
Result: ______
Evidence
overall + detail
File: _________
No verified dimensions, no approval. Measure it while the wall is still open.
14
Notes: Match the worksheet measurement log.

## Slide 15
CTS Cohort 6 | RCS02 | Day 10 | July 21, 2026
Exit ticket
Three checks before dismissal
1. Read one instructor-selected tape measurement.
2. Name the king, jack, header, sill, and plates.
3. Explain what the two diagonal measurements prove.
Tools counted. Frame flat. Evidence saved. Station reset.
15
Notes: Collect tickets and use them to decide what Day 5 needs.