## Slide 1
CTS Cohort 6 | PV101 | Day 8 | July 16, 2026
PV101 Day 8
Cumulative review, 25-question final, reflection, and closeout
SHOW WHAT YOU KNOW.
Safety first. Units count. Evidence beats labels. Work independently during the graded final.
PV101 is complete at the end of today.
1
Notes: Keep the final secured until 1:00 PM.

## Slide 2
CTS Cohort 6 | PV101 | Day 8 | July 16, 2026
Today's flow
Readiness check -> cumulative review -> final -> reflection -> closeout
Arrival
10:00
Readiness
10:20
Review
10:35
Slides
11:30
Practice
12:00
Final
1:00
Cleanup
2:55
2
The morning quiz is a short readiness check, not the final.
The final runs 1:00-2:10 and is scored out of 25.
Reflection, evidence, and cleanup formally close PV101.
Notes: Lunch is 12:30-1:00.

## Slide 3
CTS Cohort 6 | PV101 | Day 8 | July 16, 2026
The book progression
Two chapters per assigned reading day
Day 1
Ch. 1-2
Day 2
Ch. 3-4
Day 3
Ch. 5-6
Day 4
Ch. 7-8
Day 5
Ch. 9-10
Day 6
Ch. 11-12
Final: exactly two questions from each chapter, then one cumulative troubleshooting scenario.
3
Notes: This instructor-confirmed sequence overrides inconsistent legacy labels.

## Slide 4
CTS Cohort 6 | PV101 | Day 8 | July 16, 2026
Review map
Six connected skill groups
Energy path
source -> load
Electricity
V, A, W, Wh
Measurement
meter + expected value
Workmanship
mechanical + labels
Protection
fuses + disconnects
Sizing
loads -> system
4
Notes: Ask students to name one Day 1-7 example for each group.

## Slide 5
CTS Cohort 6 | PV101 | Day 8 | July 16, 2026
Core formulas
Write the formula, substitute values, keep the unit
Power
W = V x A
Energy
Wh = W x h
Battery capacity
Ah = Wh / V
Array estimate
W = Wh / PSH
1 kW = 1,000 W.
Series voltage adds; matched parallel current adds.
A number without its unit is incomplete evidence.
5
Notes: Use examples similar in skill but not identical to test items.

## Slide 6
CTS Cohort 6 | PV101 | Day 8 | July 16, 2026
Meter discipline
The meter answers a specific question
1
Question
What do I expect?
2
Function
VDC, VAC, ohms, continuity?
3
Ports + range
Leads correct?
4
Energy state
Live voltage or de-energized continuity?
5
Probe points
Exactly where?
6
Evidence
Expected vs actual
6
Notes: Continuity tests require a de-energized circuit.

## Slide 7
CTS Cohort 6 | PV101 | Day 8 | July 16, 2026
Workmanship is electrical quality
A good circuit must also be serviceable
Correct stripping and crimping; no nicked strands or exposed copper.
Tug-test terminations and support conductors mechanically.
Route for service without strain or confusion.
Label conductors, protection, disconnects, and test points.
Document the restored known-good state after work.
Cleanup and documentation are part of the technical task.
7
Notes: Tie back to Days 3-5 without repeating those labs.

## Slide 8
CTS Cohort 6 | PV101 | Day 8 | July 16, 2026
Protection: follow the source
A fuse protects the conductor; a disconnect creates a controllable state
Battery / source
Fuse close to source
Protected conductor
Equipment / load
Never bypass protection to “see if it works.”
A label is a clue, not proof.
After replacement, find the cause and verify restoration.
8
Notes: Recall Day 6 continuity evidence without recreating the fuse race.

## Slide 9
CTS Cohort 6 | PV101 | Day 8 | July 16, 2026
Troubleshooting chain
One test should separate likely causes
1
Observe symptom
2
Make system safe
3
Trace actual path
4
Predict expected value
5
Test one point
6
Document + verify
Do not replace several parts at once. That destroys the evidence trail.
9
Notes: Use expected-versus-observed language.

## Slide 10
CTS Cohort 6 | PV101 | Day 8 | July 16, 2026
Series and parallel connections
Keep voltage, current, and documented equipment limits separate
Series
voltage adds
current stays limited
Parallel
current adds
voltage stays matched
Check ratings
from actual labels
and instructions
Connection rules support diagnosis; equipment boundaries still come from documented ratings.
10
Notes: Keep the review at the PV101 fundamentals level.

## Slide 11
CTS Cohort 6 | PV101 | Day 8 | July 16, 2026
Sizing review
Loads first, assumptions visible
1
List W + hours
Show formula + unit
2
Calculate Wh/day
Show formula + unit
3
Apply autonomy + usable fraction
Show formula + unit
4
Convert Wh to Ah
Show formula + unit
5
Use PSH + loss input
Show formula + unit
6
Check concurrent W + surge
Select inverter from power
11
Notes: Review Day 7 worksheet method, not exact final answers.

## Slide 12
CTS Cohort 6 | PV101 | Day 8 | July 16, 2026
Final assessment
25 questions | 25 points | traditional graded test
16
multiple choice
4
calculations
2
diagram / sequence
2
short explanations
1
integrative scenario
Work independently.
Show formulas and units.
Ask for clarification of directions only.
Turn in the final before starting reflection.
12
Notes: Keep answer key separate. Record the raw score out of 25.

## Slide 13
CTS Cohort 6 | PV101 | Day 8 | July 16, 2026
After the final
Collection -> reflection -> evidence -> closeout
Collect + count
all tests and scratch pages
Reflect
growth + practice needs
Submit evidence
secure graded work
Reset room
PV101 complete
No mandatory correction or retest cycle. Note issues for instructor review.
13
Notes: Do not review final answers publicly unless separately directed later.

## Slide 14
CTS Cohort 6 | PV101 | Day 8 | July 16, 2026
PV101 complete
Close the course simply and professionally
YOU COMPLETED PV101.
Safety. Measurement. Workmanship. Protection. Troubleshooting. Sizing.
Reflection submitted. Materials counted. Tests secured. Tables clear.
14
Notes: Cleanup begins at 2:55. State plainly that PV101 is complete.