## Slide 1
CTS Cohort 6 | RCS06 | Day 14 | July 28, 2026
RCS Day 6
Pre-cover QC, opening layout, drywall cutting, fastening, and dust control
INSPECT BEFORE YOU COVER.
Hidden work gets verified and photographed before the panel goes on.
Today the goal is not to hide the wall. The goal is a finish-ready surface over verified work.
1
Notes: Open with the corrected lab mission. All kits remain disconnected until approval.

## Slide 2
CTS Cohort 6 | RCS06 | Day 14 | July 28, 2026
Today's flow
Quiz -> model -> guided practice -> capstone lab -> QC
Quiz
10:15
Pre-cover
10:50
Cut demo
11:20
Fastener QC
12:00
Fit panel
1:00
Inspect
2:25
Exit
2:45
Morning: inspect rough-in, transfer openings, and plan dust control.
Afternoon: cut, dry-fit, fasten, and correct one 4 ft x 3 ft panel.
End: finish-readiness evidence and controlled cleanup.
2
Notes: Use this to keep Rich and students oriented.

## Slide 3
CTS Cohort 6 | RCS06 | Day 14 | July 28, 2026
Today's targets
What successful work must demonstrate
Pre-cover
inspection
Panel +
reference edges
Window + box
openings
Fasteners
+ supports
Dust control
+ evidence
Complete a pre-cover inspection of framing and rough-in
Measure and cut a 4-foot by 3-foot drywall panel
Fit the panel around the window and device boxes
Fasten and prepare the surface for finishing
3
Notes: Emphasize the inverter is not a tiny controller load.

## Slide 4
CTS Cohort 6 | RCS06 | Day 14 | July 28, 2026
The day's path
Trace the work before building it
Inspect
rough-in
Measure
openings
Mark +
verify
Score / snap
+ cutouts
Dry-fit +
fasten
Transfer dimensions carefully and dry-fit before fastening. Protect hidden systems from blades and screws.
4
Notes: Ask students to point out positive and negative paths.

## Slide 5
CTS Cohort 6 | RCS06 | Day 14 | July 28, 2026
Controlled sequence
Release each stage only after its check
1
Pre-cover signoff
2
Opening layout
3
Cut + dry-fit
4
Fasten + inspect
Work from a supported position. Correct a bad fit before driving fasteners around the opening.
5
Notes: Say “most controllers” because manuals vary. Teach general practice plus verify equipment.

## Slide 6
CTS Cohort 6 | RCS06 | Day 14 | July 28, 2026
Working roles
6 students; every result receives another set of eyes
Installer
measures + fits
Inspector
checks openings + fasteners
Documenter
records signoffs + photos
Use partner handling when needed.
The Inspector verifies the opening map before cutting.
No panel covers unsigned rough-in.
6
Notes: This matches the actual five-kit/six-student constraint.

## Slide 7
CTS Cohort 6 | RCS06 | Day 14 | July 28, 2026
Verification checkpoints
Do not trust appearance alone
Pre-cover signed
Opening locations
Fastener dimples
Edges + cleanup
A correct fastener dimples the face without tearing it.
High and overdriven fasteners require correction before finish readiness.
7
Notes: Have students practice the measurement sentence.

## Slide 8
CTS Cohort 6 | RCS06 | Day 14 | July 28, 2026
Safety boundaries
The lab begins only inside these controls
Eye protection
Dust controls + SDS
Panel handling
Blade control
Use product- and task-appropriate ventilation, housekeeping, and PPE. Retract blades when not in use. Keep cut paths clear of hidden systems.
8
Notes: Do not overdo calculations today. Keep the principle concrete.

## Slide 9
CTS Cohort 6 | RCS06 | Day 14 | July 28, 2026
Professional judgment
Safe work pauses when the evidence conflicts
Good fastener
slight dimple; paper intact
Rejected fastener
high or paper torn
Fastener quality is visible evidence. Dry-fit openings and edges before committing the panel to the wall.
9
Notes: Unless the equipment manual says otherwise, teach inverter battery-side with protection.

## Slide 10
CTS Cohort 6 | RCS06 | Day 14 | July 28, 2026
Quality criteria
Good physical work leaves visible proof
Sign the pre-cover checklist.
Measure openings from two reference edges.
Score, snap, back-cut, and support the panel.
Fasten without tearing face paper.
Inspect, correct, control dust, and reset.
Unsigned rough-in? Do not cover it.
10
Notes: Make rework normal. Bad crimps are data. Hidden bad crimps are future pain.

## Slide 11
CTS Cohort 6 | RCS06 | Day 14 | July 28, 2026
Lab release checklist
The station earns work only after the checks
Framing and rough-in pre-cover check passed.
Panel and openings measured twice.
Cutout marks partner-verified.
Cut path protects boxes and hidden systems.
Dust controls and PPE are active.
Panel handling plan is clear.
11
Notes: Use this slide as the afternoon pass standard.

## Slide 12
CTS Cohort 6 | RCS06 | Day 14 | July 28, 2026
Afternoon lab
Slow sequence. Clear callouts. No surprises.
1
Inspect + photograph
2
Measure + mark
3
Cut + dry-fit
4
Fasten + finish QC
Fit and fasten drywall over the individual capstone wall while preserving the window and device-box openings.
12
Notes: Keep control of the final power-up moment.

## Slide 13
CTS Cohort 6 | RCS06 | Day 14 | July 28, 2026
Closeout order
End verified, documented, and reset
1
Check openings
2
Check fasteners
3
Correct defects
4
Clean + document
Leave the surface finish-ready: secure board, supported edges, clean openings, correct fasteners, and recorded corrections.
13
Notes: Use this before cleanup so the room ends clean.

## Slide 14
CTS Cohort 6 | RCS06 | Day 14 | July 28, 2026
Evidence log
What students write down
Pre-cover
signed + photo
Initials: ______
Panel
4 ft x 3 ft
Measure: _____
Window
location + fit
Gap: _________
Boxes
clear + undamaged
Pass: ________
Fasteners
dimple + spacing
Pass: ________
Cleanup
dust controlled
Complete: _____
No pre-cover signoff, no panel. No finish-readiness inspection, no approval.
14
Notes: Match the worksheet measurement log.

## Slide 15
CTS Cohort 6 | RCS06 | Day 14 | July 28, 2026
Exit ticket
Three checks before dismissal
1. Name one pre-cover item that must be verified.
2. Describe a correct drywall fastener dimple.
3. State the dust-control and blade-control plan.
Panel secure. Openings clear. Dust controlled. Evidence saved.
15
Notes: Collect tickets and use them to decide what Day 5 needs.