## Slide 1
Day 38 EBIKE101
E-bike Homunculous Diagnosis
Find what is present, what is missing, what is unsafe, and what needs finishing before power or riding.
Tuesday | 2026-09-08

## Slide 2
CTS Cohort 6 | EBIKE101 | Day 38
Today’s real job
• Diagnose the unfinished e-bike build without guessing.
• Build a parts and finish-work list.
• Begin safe approved work only after inspection.
• Document every symptom, measurement, and decision.

## Slide 3
CTS Cohort 6 | EBIKE101 | Day 38
The diagnosis rule
• Inventory first.
• De-energize before continuity testing.
• Trace source → protection → control → load.
• Power testing comes after mechanical and electrical checks.

## Slide 4
CTS Cohort 6 | EBIKE101 | Day 38
System inventory
• Battery present and voltage known?
• Fuse or breaker present and correctly placed?
• Controller mounted and labeled?
• Display, PAS, throttle, brake cutoffs identified?
• Motor cable protected from pull, rub, and wheel movement?

## Slide 5
CTS Cohort 6 | EBIKE101 | Day 38
Likely failure points
• Blown fuse or bad fuse holder.
• Loose or mismatched connector.
• Missing throttle or control input.
• Brake cutoff stuck active.
• PAS sensor misaligned.
• Battery switch, BMS, or connector not passing power.

## Slide 6
CTS Cohort 6 | EBIKE101 | Day 38
Safety boundary
• No ride testing until instructor clears it.
• No live continuity tests.
• No bypassing fuses.
• No “larger fuse fixes it” nonsense.
• No hands near moving chain, wheel, or rotor during powered tests.

## Slide 7
CTS Cohort 6 | EBIKE101 | Day 38
Team roles
• Lead diagnostician: keeps the fault tree organized.
• Meter lead: takes and calls out measurements.
• Recorder: logs symptoms, measurements, changes, and next step.
• Safety spotter: watches hands, wheels, cables, and battery state.

## Slide 8
CTS Cohort 6 | EBIKE101 | Day 38
Fault tree order
• 1. Mechanical safe to inspect?
• 2. Battery and protection path verified?
• 3. Controller powered?
• 4. Display wakes?
• 5. Inputs identified?
• 6. Motor phases/hall/PAS/brake signals checked?
• 7. Safe low-power test approved?

## Slide 9
CTS Cohort 6 | EBIKE101 | Day 38
Finish-work list
• Must finish before power.
• Must finish before ride.
• Nice to improve if time allows.
• Parts/tools needed.
• Final verification evidence needed.

## Slide 10
CTS Cohort 6 | EBIKE101 | Day 38
The lesson underneath
• The smallest cheapest part can stop the largest expensive system.
• A hidden bad fuse can look like a dead motor, controller, or battery.
• Good technicians verify before replacing expensive parts.
• Documentation turns chaos into progress.

## Slide 11
CTS Cohort 6 | EBIKE101 | Day 38
Exit target
• By the end of class, every team should know:
• What works.
• What does not work yet.
• What is missing.
• What must be verified before power or riding.
• What the next safe work step is.