## Slide 1
RCS Day 1
Residential Systems & Shop Safety
CTS Cohort 6 | Monday, July 20, 2026
Today's rule:
A professional does not guess. A professional checks, protects, and verifies.
Structure
Electrical
Plumbing
Finish
One building. Many systems. One standard: verify before covering.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Notes: Open calm. Tell students this module is hands-on but not rushed. The first day is about how professionals move around tools, systems, and each other.

## Slide 2
Today's flow
Start safe, learn the system, then build and test a simple plumbing assembly.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
1
10:00
Arrival + safety reset
2
10:15
RCS overview
3
10:40
PPE + shop rules
4
11:10
Power tool intro
5
11:35
Quiz + review
6
12:30
Rolling sink lab
7
2:35
Document + cleanup
8
2:50
Exit ticket
Quiet quiz first. Hands-on work after the safety frame is clear.
Notes: Use this slide to lower anxiety. Students should know the shape of the day before tools come out.

## Slide 3
Learning targets
By dismissal, students should be able to do these without guessing.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Name the major residential building systems.
Select PPE for common shop tasks.
Explain stop-work authority and tool accountability.
Identify common power tools and their main hazards.
Assemble a simple sink drain and P-trap.
Leak test, correct, and document the assembly.
Today is about professional habits before capstone work starts.
Notes: These are the whole day. Keep referring back to them during lab and cleanup.

## Slide 4
What RCS means in CTS
Residential Construction Specialty is where technical habits become jobsite habits.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Work habits
Trade content
Measure before cutting
Inspect before covering
Communicate before moving material
Clean before calling a task finished
Framing
Electrical rough-in
Plumbing basics
Drywall and inspection
The habit is the portable skill.
Notes: Frame RCS as a continuation of CTS, not a new unrelated class.

## Slide 5
The final wall project starts today
Every day points toward the individual 4 ft x 3 ft wall build.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Frame a small wall section.
Build a window rough opening.
Install two receptacle boxes.
Install one switch and light circuit.
Drywall the whole board with proper cutouts.
Explain and inspect the finished work.
4 ft x 3 ft
individual wall
Notes: Make the capstone concrete now. Students should know why Day 1 matters.

## Slide 6
Residential systems map
Buildings are not random parts. They are connected systems.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Structure
Electrical
Plumbing
HVAC
Envelope
Finish
A good builder understands what will be hidden, protected, or affected by the next trade.
Notes: Ask students for examples of each system. Keep it practical and familiar.

## Slide 7
Professional expectations
Employers notice habits before they trust skill.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Show up ready to work.
Ask before touching unknown tools or systems.
Keep your area organized enough to be safe.
Tell the truth about mistakes quickly.
Document work so another person can understand it.
Today is about professional habits before capstone work starts.
Notes: Keep this direct. RCS is about becoming employable, not just completing school work.

## Slide 8
Safety is not a speech
Safety is the way the work gets done.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
PPE
Eyes, ears, hands, lungs, and clothing match the task.
Position
Stable feet, clear hands, clear blade path, no body parts in the line of fire.
Communication
Call out before cuts, moving material, energizing, or testing.
Notes: Do not let safety become a lecture cloud. Keep it behavioral.

## Slide 9
PPE for today
Use the protection that matches the hazard. More is not always better; wrong PPE is still wrong.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Eye protection
Required during cutting, drilling, fastening, and leak-test cleanup.
Hearing protection
Required around saws and loud tools.
Gloves
Useful for carrying material. Not for rotating blades/bits.
Dust control
Drywall and cutting dust need cleanup and breathing awareness.
Notes: Demonstrate glasses, hearing protection, gloves as appropriate, and when gloves are not appropriate around rotating tools.

## Slide 10
Stop-work authority
Stopping is a skill. Guessing is not a method.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Something feels unsafe or unclear.
A tool is damaged or behaving oddly.
A cut, route, or connection does not match the plan.
Someone is in the path of material, blade, cord, water, or tool movement.
You cannot explain the next step.
Stop. Ask. Verify.
Notes: Make this explicit. Stop-work authority is not drama or getting someone in trouble.

## Slide 11
Tool accountability
A missing tool is not a mystery. It is a future problem.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
1
Check out
2
Inspect
3
Use correctly
4
Return clean
5
Report damage
Same tool. Same place. Every time.
Notes: Connect this to real shops. Tool chaos wastes time and erodes trust.

## Slide 12
Power tool safety ladder
Students earn tool use through demonstrated control, not confidence.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
1
Identify tool
2
Inspect condition
3
Set material support
4
Check body position
5
Operate slowly
6
Shut down safely
7
Clean and return
Confidence is not clearance. Demonstration is clearance.
Notes: Make clear that today is introduction and supervised demonstration. Independent use requires instructor clearance.

## Slide 13
Drill and driver safety
Small tools can still injure people and ruin work.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Correct bit or driver tip
Battery removed during bit changes
Clamp or secure material
Two hands when needed
Low speed for starting
Stop before stripping or splitting
Slow is smooth. Smooth is safe.
Notes: Use a drill/driver as the first live demonstration if available.

## Slide 14
Saw safety introduction
A saw cut is a planned movement, not a surprise event.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Know the blade path
Support both sides of material
Keep hands outside the danger zone
Wait for full stop before moving off cut
Never bypass guards
Ask before any unfamiliar cut
Slow is smooth. Smooth is safe.
Notes: Introduce circular saw, miter saw, and jigsaw only at a high level. Do not clear students for independent use without demonstration.

## Slide 15
Measurement habit
The cut is only as good as the layout.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Read the tape correctly.
Mark the waste side.
Use the square for straight lines.
Verify with a partner before cutting.
Write important dimensions down.
Mark it so someone else can understand it.
Notes: Bridge to Day 2 framing. Use a tape and speed square as visible props.

## Slide 16
Plumbing system example
Today's lab uses plumbing because leaks tell the truth quickly.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Water source
Shutoff
Faucet
Sink
Tailpiece
P-trap
Drain outlet
Supply brings clean water in. Drainage carries used water out. The trap protects the space.
Notes: Explain supply vs drain. Keep it beginner friendly.

## Slide 17
Why a P-trap exists
The bend is not decorative. It is a simple safety system.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Holds water to block sewer gas.
Creates a removable service point.
Needs correct washer orientation and tight joints.
Leaks usually come from alignment, missing washers, or overtightening.
The part has a job. Know the job before tightening.
Notes: Have students predict what the trap does before explaining. Then state it plainly.

## Slide 18
Afternoon lab mission
Rolling sink module: assemble, test, correct, document.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
1
Inventory parts
2
Dry-fit layout
3
Assemble by hand
4
Leak test
5
Troubleshoot
6
Document
7
Reset station
Build - test - correct - document.
Notes: Give students the workflow before handing out parts.

## Slide 19
Lab roles
Clear roles prevent six hands from becoming one plumbing octopus.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Builder
Assembles parts and calls out each step.
Inspector
Checks alignment, washers, tightness, and leaks.
Documenter
Records parts, problems, fixes, and evidence photos.
Notes: Assign roles even with small groups. Rotate halfway if needed.

## Slide 20
Common mistakes
Mistakes are data when they are noticed early.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Cross-threaded slip nut
Washer missing or reversed
Trap arm not aligned
Overtightened plastic fitting
No bucket or towel during testing
Leak not documented before repair
Find it early. Fix it clean.
Notes: Show examples if you have old fittings. This prevents shame during leaks.

## Slide 21
Verification checkpoint
Stop before water. Inspect before testing.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
All washers present and facing correctly.
Slip nuts started straight.
Trap path can be explained.
Bucket/towel ready.
Instructor or peer check complete.
No water until the path makes sense.
Notes: This is the key lab pause. No water until the group can explain the assembly.

## Slide 22
Verification log
Documentation is safety support, not paperwork theater.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
What I checked
What I expected
What I observed
Tool or method used
What I corrected
What still needs checking
If it is not documented, the next person has to guess.
Notes: Show students the exact kind of entry you want.

## Slide 23
Cleanup standard
The job is not done until the next person can start safely.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Water off and area dry
Parts counted and returned
Tools cleaned and stored
Floor clear of trip/slip hazards
Evidence uploaded or turned in
Reset is part of the work.
Notes: Make cleanup part of grading and professional habits.

## Slide 24
Exit ticket
Write complete sentences. Short is fine. Vague is not.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
One residential system I can name is...
One safety rule I need to remember is...
One thing I verified during lab was...
One thing I want more practice with is...
This tells us what to reteach.
Notes: Give students quiet time. This checks what landed and what needs reteaching tomorrow.

## Slide 25
Tomorrow preview
Day 2: measuring, layout, framing, and controlled tool use.
CTS Cohort 6 | RCS Day 1 | 7/20/2026
Residential Construction Specialty
Tape measure accuracy
Speed square layout
Cut list basics
Wall parts: plates, studs, rough opening
Power tool clearance and supervised cuts
Building toward the individual wall project
Tomorrow starts the wall.
Notes: End by making tomorrow feel connected to today and the final wall.