## Slide 1
CTS Cohort 6 | RCS05 | Day 13 | July 27, 2026
RCS Day 5
Switch-controlled lighting, de-energized troubleshooting, correction, and retest
FIND THE FIRST FAILED CHECKPOINT.
One expected path. One controlled fault. One correction at a time.
Today the goal is not random fixes. The goal is evidence that explains the failure.
1
Notes: Open with the corrected lab mission. All kits remain disconnected until approval.

## Slide 2
CTS Cohort 6 | RCS05 | Day 13 | July 27, 2026
Today's flow
Quiz -> model -> guided practice -> capstone lab -> QC
Quiz
10:15
Light path
10:50
Splice demo
11:20
Fault ladder
12:00
Build
1:00
Diagnose
2:25
Exit
2:45
Morning: trace line, switch leg, load, neutral return, and grounding.
Afternoon: add switch/light boxes and diagnose an inserted fault.
End: correction, retest, evidence, label, reset.
2
Notes: Use this to keep Rich and students oriented.

## Slide 3
CTS Cohort 6 | RCS05 | Day 13 | July 27, 2026
Today's targets
What successful work must demonstrate
Line
source path
Switch
control
Switch leg
to load
Light
load
Neutral +
ground paths
Trace a de-energized switch-controlled lighting path
Install a training switch and light outlet box
Use visual inspection and continuity to diagnose inserted faults
Document the fault, evidence, correction, and retest
3
Notes: Emphasize the inverter is not a tiny controller load.

## Slide 4
CTS Cohort 6 | RCS05 | Day 13 | July 27, 2026
The day's path
Trace the work before building it
Line
Switch
Switch leg
Light load
Neutral
return
Trace the path before testing. The first checkpoint that stops matching expectation narrows the fault location.
4
Notes: Ask students to point out positive and negative paths.

## Slide 5
CTS Cohort 6 | RCS05 | Day 13 | July 27, 2026
Controlled sequence
Release each stage only after its check
1
Isolate + verify
2
Predict checkpoints
3
Test in order
4
Correct one + retest
Students perform no energized diagnostics. Continuity is used only on isolated conductors under instructor control.
5
Notes: Say “most controllers” because manuals vary. Teach general practice plus verify equipment.

## Slide 6
CTS Cohort 6 | RCS05 | Day 13 | July 27, 2026
Working roles
6 students; every result receives another set of eyes
Builder
installs switch + light
Inspector
checks path + splices
Documenter
logs tests + correction
Rotate before the faulted state is issued.
The troubleshooter says the expected result before each test.
No one changes two conditions at once.
6
Notes: This matches the actual five-kit/six-student constraint.

## Slide 7
CTS Cohort 6 | RCS05 | Day 13 | July 27, 2026
Verification checkpoints
Do not trust appearance alone
Expected path
Known source state
First mismatch
Correction + retest
A continuity beep is evidence of a path, not permission to energize.
Record probe points, expected result, observed result, and conclusion.
7
Notes: Have students practice the measurement sentence.

## Slide 8
CTS Cohort 6 | RCS05 | Day 13 | July 27, 2026
Safety boundaries
The lab begins only inside these controls
Mock-up isolated
No energized diagnostics
Continuity only isolated
Instructor controls fault
Treat any unverified conductor as energized. Replace damaged devices or conductors. Close and label the training system after approval.
8
Notes: Do not overdo calculations today. Keep the principle concrete.

## Slide 9
CTS Cohort 6 | RCS05 | Day 13 | July 27, 2026
Professional judgment
Safe work pauses when the evidence conflicts
Good method
predict -> test -> locate -> correct
Bad method
change everything -> lose evidence
Troubleshooting is controlled comparison. One change at a time preserves cause-and-effect evidence.
9
Notes: Unless the equipment manual says otherwise, teach inverter battery-side with protection.

## Slide 10
CTS Cohort 6 | RCS05 | Day 13 | July 27, 2026
Quality criteria
Good physical work leaves visible proof
Trace line-switch-load-neutral first.
Prepare splices and pigtails cleanly.
Inspect boxes and terminations.
Test only the isolated expected path.
Correct, retest, document, and obtain approval.
No expected result? Do not place the probes.
10
Notes: Make rework normal. Bad crimps are data. Hidden bad crimps are future pain.

## Slide 11
CTS Cohort 6 | RCS05 | Day 13 | July 27, 2026
Lab release checklist
The station earns work only after the checks
Energy state verified and called out.
Switch/light path matches the diagram.
Boxes, cable, and splices inspected.
Expected checkpoints written before testing.
Continuity used only while isolated.
Instructor controls fault insertion and reset.
11
Notes: Use this slide as the afternoon pass standard.

## Slide 12
CTS Cohort 6 | RCS05 | Day 13 | July 27, 2026
Afternoon lab
Slow sequence. Clear callouts. No surprises.
1
Install switch + light
2
Inspect + isolate
3
Diagnose inserted fault
4
Correct + retest
Add the switch and light point to the capstone, then diagnose one instructor-inserted open or misconnection.
12
Notes: Keep control of the final power-up moment.

## Slide 13
CTS Cohort 6 | RCS05 | Day 13 | July 27, 2026
Closeout order
End verified, documented, and reset
1
Name the fault
2
Show the failed checkpoint
3
Show the correction
4
Show the retest
The repair is not complete until the result is retested, documented, labeled, and instructor-approved.
13
Notes: Use this before cleanup so the room ends clean.

## Slide 14
CTS Cohort 6 | RCS05 | Day 13 | July 27, 2026
Evidence log
What students write down
Energy
isolated + known
Initials: ______
Path
line to neutral
Pass: ________
Visual
boxes + splices
Pass: ________
Checkpoint
first mismatch
Point: _______
Correction
one change
Action: ______
Retest
expected restored
Result: _______
A guess is not a diagnosis. Record the checkpoint that proves the fault and the retest that proves the correction.
14
Notes: Match the worksheet measurement log.

## Slide 15
CTS Cohort 6 | RCS05 | Day 13 | July 27, 2026
Exit ticket
Three checks before dismissal
1. Draw line -> switch -> load -> neutral return.
2. Identify the first failed checkpoint in your fault.
3. State the evidence that proved your correction.
System isolated. Fault logged. Correction retested. Boxes closed.
15
Notes: Collect tickets and use them to decide what Day 5 needs.