## Slide 1
PV101 Day 3
2026-07-08 | Tim with trail crew
Rich leads today
Morning: Chapters 3-4 reading quiz
Afternoon: wire stripping and crimping lab
6 students: 2 groups of 3

## Slide 2
Today's Target
Understand the solar system path
Use PV vocabulary without guessing
Prepare wire cleanly
Make and inspect crimped practice connections
Slow is smooth. Smooth becomes reliable.

## Slide 3
Morning Quiz
Based on Solar Photovoltaics Basics, Chapters 3 and 4
Individual first
Review together after
Correct mistakes in a different color
Missed questions tell us what to reteach

## Slide 4
PV System Path
Draw this before explaining details
Sun
PV Module
Charge Controller
Battery
DC Loads
Inverter
AC Loads
Keep asking: What is the source? What stores energy? What controls it? What uses it?

## Slide 5
Reading Frame: Chapters 3-4
Sunlight is the resource
PV cells convert light into DC electricity
Modules combine cells
Arrays combine modules
System parts control, store, and use energy

## Slide 6
Solar Resource Words
Irradiance: sunlight power right now
Insolation: solar energy over time
Both affect how much useful energy a PV system can make
Weather, tilt, direction, and shade all matter

## Slide 7
Power Language
Voltage = electrical pressure
Current = electrical flow
Power = work being done
Watts = Volts x Amps
Energy = power over time

## Slide 8
Why Wire Prep Matters
Bad wiring creates unreliable systems
Loose connections become troubleshooting nightmares
Clean work is easier to inspect
Serviceability matters for the next person

## Slide 9
Strip Quality
Good connections start before the crimp
Bad: too much copper
Good: clean strip
Bad: damaged strands
Inspect before crimping. If it looks wrong now, it will not become right later by wishing. Humans keep trying this anyway.

## Slide 10
Crimping Rules
Match connector to wire size
Insert wire fully
Crimp on the metal barrel
Use the correct die/slot
Do not crimp loose insulation and call it optimism

## Slide 11
Tug Test + Visual Check
Pull with reasonable hand force
Connector should not slide off
No bare copper hairs sticking out
No missing strands
Connection should be easy to inspect later

## Slide 12
Lab Groups
Group A: 3 students
Group B: 3 students
Roles: Tool Lead, Quality Inspector, Recorder
Rotate after each completed connection

## Slide 13
Lab Rule
Practice wire only
No live circuits
No unknown equipment
Ask Rich before changing wire, connector, or tool
Quality before speed

## Slide 14
Exit Ticket
One thing I can do now
One thing I still need to practice
Why clean wiring matters in RV solar
Tools counted and benches cleaned before leaving