## Slide 1
EBIKE101 Day 3
Motors, Controllers, Throttle/PAS, and Signal Flow
Trace the system before you test the system.
EBIKE101 Day 3 | 1/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 2
Today's question
How does rider input become controlled wheel motion, and where can that chain fail?
Day 35 | Wednesday, September 2, 2026
EBIKE101 Day 3 | 2/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 3
Core rule
Power off first.
Trace before testing.
Control motion before adding power.
Unknown connector or unexpected motion means stop-work.
EBIKE101 Day 3 | 3/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 4
Two paths work together
The power path carries energy. The signal path tells the controller what to do.
Do not confuse a command with the energy that performs it.
EBIKE101 Day 3 | 4/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 5
The motor makes torque
The motor converts controlled electrical energy into mechanical rotation.
The motor moves only after the rest of the system agrees.
EBIKE101 Day 3 | 5/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 6
Hub drive and mid-drive
Hub motors turn a wheel. Mid-drives add torque through the bicycle drivetrain.
Different locations change mounting, service, and load paths.
EBIKE101 Day 3 | 6/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 7
The controller decides
It reads rider and safety inputs, then controls battery power sent to the motor.
A controller is the traffic cop between command and motion.
EBIKE101 Day 3 | 7/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 8
Rider inputs
Throttle asks directly. PAS detects pedaling. The display sets modes and limits.
Inputs request motion. They do not make safe motion automatic.
EBIKE101 Day 3 | 8/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 9
Brake cutoffs say stop
When installed, a brake cutoff tells the controller to stop driving the motor.
A safety input should override a go input.
EBIKE101 Day 3 | 9/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 10
Power path
Battery -> fuse or protection -> controller -> motor -> mechanical rotation
This path carries the energy that does the work.
EBIKE101 Day 3 | 10/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 11
Signal path
Throttle, PAS, brakes, and display -> controller decision
A tiny signal can command a much larger power path.
EBIKE101 Day 3 | 11/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 12
Connector boundary
Never force, guess, back-probe, or disconnect an energized connector without approval.
Match shape, pin count, keying, labels, and wire routing.
EBIKE101 Day 3 | 12/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 13
Diagnostic order
1. Make safe
2. Confirm the complaint
3. Trace the path
4. Test one point at a time
Check the system in order instead of replacing parts by mood.
EBIKE101 Day 3 | 13/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 14
Team roles
Tracer. Connector inspector. Diagrammer. Reporter.
Every person owns one part of the evidence.
EBIKE101 Day 3 | 14/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 15
Lab A
Identify every control and power component.
Battery, controller, motor, display, throttle/PAS, brake cutoffs, connectors.
EBIKE101 Day 3 | 15/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 16
Lab B
Draw the power path and signal path separately.
Then show where both paths meet at the controller.
EBIKE101 Day 3 | 16/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 17
Lab C
Trace one no-assist fault without swapping parts.
Prove each checkpoint before moving to the next one.
EBIKE101 Day 3 | 17/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 18
Winning condition
Name the path. Mark the checkpoints. Explain the first safe test.
Evidence first. Motion last.
EBIKE101 Day 3 | 18/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 19
Tomorrow
Battery, BMS, charging, connectors, and electrical safety.
Stored energy gets its own rules because it keeps working after class ends.
EBIKE101 Day 3 | 19/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.

## Slide 20
Quote of the day
Trace the system. Do not guess at it.
EBIKE101 | CTS Cohort 6
EBIKE101 Day 3 | 20/20
Notes: [Sources]
- Internal curriculum source: EBIKE101 8-Day Curriculum Map and Day 1 continuity package.