## Slide 1
EBIKE101 Day 1
Introduction, Rider Safety, and System Inspection
Safe micro-mobility starts before the throttle moves.
EBIKE101 Day 1 | 1/20

## Slide 2
Today's question
What makes an e-bike different from a bicycle, and what must be proven safe before anybody rides it?
Day 33 | Monday, August 31, 2026
EBIKE101 Day 1 | 2/20

## Slide 3
Core rule
No ride.
No throttle test.
No powered wheel spin.
Until the bike passes a visible safety check.
EBIKE101 Day 1 | 3/20

## Slide 4
A bicycle is already a system
Frame, fork, wheels, tires, brakes, drivetrain, cockpit, and rider contact points.
Electricity does not fix loose wheels.
EBIKE101 Day 1 | 4/20

## Slide 5
An e-bike adds more systems
Battery, controller, motor, display, throttle or pedal assist, wiring, connectors, charger, and cutoffs.
More capability means more inspection. Amazing how physics keeps having opinions.
EBIKE101 Day 1 | 5/20

## Slide 6
Conventional bike checks
Tires. Brakes. Wheels. Steering. Drivetrain. Seat. Pedals. Frame and fork.
If the bicycle is unsafe, the e-bike is unsafe.
EBIKE101 Day 1 | 6/20

## Slide 7
E-bike system checks
Battery condition. Battery mount. Controller mount. Wiring path. Connectors. Display. Throttle or PAS. Charger.
Turning on is not the same as safe.
EBIKE101 Day 1 | 7/20

## Slide 8
Basic flow
Rider input -> controller -> battery power -> motor -> wheel motion
The rider asks. The controller decides. The motor moves.
EBIKE101 Day 1 | 8/20

## Slide 9
Battery boundary
No swollen, hot, damaged, wet, unknown, or mismatched battery or charger gets used.
Stored energy deserves respect.
EBIKE101 Day 1 | 9/20

## Slide 10
Wiring boundary
No wires near tires, chains, cranks, brake rotors, sharp edges, heat, or pinch points.
Loose wires are future problems volunteering early.
EBIKE101 Day 1 | 10/20

## Slide 11
Pre-ride categories
Mechanical. Electrical. Rider control. Area and route. Documentation.
Pass, fail, or instructor review. No fantasy category called “probably fine.”
EBIKE101 Day 1 | 11/20

## Slide 12
Stop-work triggers
Unexpected motion. Loose battery. Failed brakes. Wheel rub. Damaged wiring. Unknown charger. Unsafe joke becoming unsafe behavior.
Pause the work before the work teaches the lesson the hard way.
EBIKE101 Day 1 | 12/20

## Slide 13
Team roles
Inspector 1: mechanical
Inspector 2: electrical
Recorder: notes
Reporter: debrief
Roles keep the lab from becoming six humans orbiting one bike.
EBIKE101 Day 1 | 13/20

## Slide 14
Lab A
Inspect the mechanical bike first.
Frame, fork, wheels, tires, brakes, steering, drivetrain, contact points.
EBIKE101 Day 1 | 14/20

## Slide 15
Lab B
Inspect the e-bike systems second.
Battery, motor, controller, wiring, connectors, display, throttle/PAS, charger, cutoffs.
EBIKE101 Day 1 | 15/20

## Slide 16
Lab C
Draw the system flow and mark what could fail.
Input -> control -> power -> motion -> rider.
EBIKE101 Day 1 | 16/20

## Slide 17
Winning condition
Find it. Name it. Document it. Explain the safe next step.
No guessing. No sending it. Humanity has tested that.
EBIKE101 Day 1 | 17/20

## Slide 18
Debrief questions
What mechanical risk did you find?
What electrical risk did you find?
What rider-control risk did you find?
What must be checked first tomorrow?
EBIKE101 Day 1 | 18/20

## Slide 19
Tomorrow
Bicycle mechanics foundations.
Before conversion, the bike itself has to be worthy of electricity.
EBIKE101 Day 1 | 19/20

## Slide 20
Quote of the day
Power only comes after control is proven.
EBIKE101 | CTS Cohort 6
EBIKE101 Day 1 | 20/20